## Slide 1: PGC-D3 – Small Scale LNG Subgroup Asia Pacific & Middle East
13-16 May 2014
Osaka, Japan

## Slide 2: Scope
Progress report on data collection in the sub group Asia Pacific & Middle East
Outline
Data have been collected for geographical area Asia Pacific & Middle East with respect to all the topics specified in the template distributed after kick-off meeting
Countries screened: Australia, New Zealand, China, India, Indonesia, Japan, South Korea, Taiwan, Thailand, Brunei, Malaysia, Myanmar, Taiwan, Vietnam, Pakistan, Bangladesh, Singapore, Philippines, Nepal, Bhutan and Middle East

## Slide 3: Mind Map -Scope of the Subgroups
Definition
Size, layout
Current status
Value Chain
Supply (Liquefaction, stranded gas, pipeline gas, associated gas, flare gas)
Midstream/Transport (barges, ships, trucks, trains)
Drivers, Purpose
Environmental, Economic, Gas Monetisation, Security of Supply, Growth of Demand, Regulatory Environment, Phasing, Geography, CAPEX/OPEX, local distribution for remote areas, Grid Balancing, tuning overall Mix, Bridge Supply
Downstream/End Users
Business Model
Players, Markets, Costs, Enablers, Competition, Standardization
Support with case studies
Technology
Size, Process, Efficiency, Safety
SMALL SCALE LNG

## Slide 4: Summary of major findings/trends per country
Refer to excel file for all detailed information gathered
13-16 May 2014
Osaka, Japan

## Slide 5: Australia & New Zealand
Australia:
4 existing SSLNG projects with dedicated plants for liquefaction of pipeline gas known and listed
liquefaction capacity 50 to 200 tpd
major purpose: peak shaving, remote power generation, truck fuelling
no concrete planned/new projects found
New Zealand:
no activity found in New Zealand

## Slide 6: China
by far the largest and most dynamic market for SSLNG in Asia Pacific, maybe even worldwide
current own market assessment preliminary due to large number of identified projects and difficult to verify sources of information
a number of approx. 100 small scale liquefaction plants seem to be existing or close to start of operation with a total design liquefaction capacity of approx. 44 Mill Nm3/d or 12 mtpa!
another 50-70 projects in the planning stage with a total liquefaction capacity of approx. 15 mtpa could be found in the local media

## Slide 7: China
a 2014 report from FACTS states 65 plants in operation, 34 under construction and a total liquefaction capacity of 17 mtpa by end 2014
Wood Mackanzie forecasts market for gas in transport in China to 45 Bcm by 2030
plant capacities range from 0,005 to 0,5 mtpa (15 to 1.500 tpd) in a single train
a significant number of plants seem to suffer from insufficient feed stock supply and/or not adequately developed downstream market, hence actually produced amount will be partly lower than design value
localization of the LNG industry is politically pushed

## Slide 8: China
major purpose of the plants: fuelling of large truck fleets (approx. 30% cost savings in comparison to diesel)
favorable economics:
  low cost of vehicles
  strong vehicle market growth encouraging fleet investments in gas
  financial support from regional governments to reduce emissions in cities to reduce pollution/smog
other utilization of LNG: peak-shaving, residential and industrial use

## Slide 9: China
diverse feed stock: pipeline gas, SNG from coal gasification, CBM, coke gas
the excel file includes all known plants/projects with a liquefaction capacity of more than 250.000 tpa, which are mainly based on international liquefaction technology, however a first plant based on Chinese technology with 0,5 mtpa capacity went in operation in 2012 and another one with total 1,4 mtpa in 5 trains is close to commissioning

## Slide 10: India
Indian Oil Corporation Limited, India pioneered the marketing & distribution of LNG by road during 2007 from Dahej LNG Terminal (imported LNG)
Around 35 tankers are in operation in India
PLL set up LNG loading facilities at LNG Terminal at Dahej in Gujarat
8-10 trucks per day which accounts for around 2800 – 3000 loads per year
Presently LNG (by road tanker) is being sold to stranded customers away from pipeline in Western region like Gujarat, Maharashtra, Madhya Pradesh, Silvassa, Rajasthan and Karnataka in Southern Region
Primarily, LNG is being used as substitute for alternative conventional fuel
Similar activity of LNG distribution by road is expected to be commenced from LNG Terminal at Kochi, Kerala early next year
Inland "Hub and Spoke" is under execution
In 3-4 years approx. 1mtpa LNG are expected to be distributed by road; major obstacle is price level of LNG in comparison to conventional fuels

## Slide 11: Indonesia
no existing SSLNG project found
5 mini LNG receiving terminals (5-30 mmscfd) planned by Pertamina, mainly in Kalimantan and East Sulawesi
LNG supply from Bontang by sea and land
major purpose: remote power generation and mining industry

## Slide 12: Japan
1 small scale liquefaction plant (350 tpd) and 6 small scale 'secondary' import terminal projects (2.300 to 10.000 m3 storage volume) existing
LNG distribution mainly by coastal small scale LNG vessel
major purpose: power production, wholesale, retail
1 planned small scale LNG import terminals identified
initial Japanese team member unfortunately not supportive anymore

## Slide 13: South Korea
100tpd liquefaction plant built by Kogas with own SMR technology (Government supported) at Incheon LNG Receiving Terminal (envisaged start-up 4/2013)

## Slide 14: Thailand
one small scale natural gas liquefaction plant (18 tpd) in operation by PTT
major purpose: NGVs, LNG fuelled boat
driver: pollution control
project has to be regarded as demonstration project
no new planned project identified

## Slide 15: Malaysia
1.2 mtpa FLNG project offshore Sarawak (Kanowit) in execution phase (envisaged start-up 4/2015)
Purpose: Monetise stranded upstream gas assets

## Slide 16: No small scale activity identified in ...
Brunei, Myanmar, Taiwan, Vietnam, Pakistan, Bangladesh, Singapore, Philippines*, Nepal, Bhutan and Middle East countries
* one small scale LNG plant with 25 tpd liquefaction capacity based on biogas in execution since early 2014 for Batangas

## Slide 17: Safety, Standards and Regulations
  China: no LNG standard issued yet; local GB codes for the petrochemical industry are applied
  Thailand: safety, standards and regulation are still based on international standards and operate under Thai government regulation