## Slide 1: PGC-D3 – Small Scale LNG Definition and Technology Subgroup Definition elements and specific features
14th - 16th May 2014
Osaka, Japan

## Slide 2: Elements of definition (1)
 Picture of a growing business, still evolving.
 review/refine the boundaries will in all probability occur.
 LNG used to be small scale (first ship <10% of the current average standard)
 Downscaling is challenging to stay profitable
1 MTPA just provide a contour  definition is not frozen  no market marker yet.
Subcategories will be defined by the technical/cost limitation all along the chain and the associated logistic.

## Slide 3: Elements of definition (2)
End users:
  Regular consumption of LNG / aging  constraints in sizing
  Cryogenic specificity : LNG can never be store for long (without reliquefying it).
  From big to small
    industrial/independent producers,
    ships and barges using LNG as fuel,
    road transportation (truck and cars). Trains are not yet a significant reality but could become more concrete soon.
Logistic: existing infrastructures  role in limiting volume handled (size of road is an).
Producers: sizes are chosen so as to maintain the plant profitable.
Annual capacity (MTPA) | 1 | 0.5 | 0.1
Conventional LNGC (170k)/y | 15 | 7 | 1
Small LNGC (30k)/y | 82 | 41 | 8
Very Small LNGC (5k)/y | 455 | 228 | 46
Trucks (50m3):y | 45455 | 22728 | 4546
Trucks (50m3)/day | 125 | 63 | 13

## Slide 4
Small Regas Terminal (1)
Common features, most of the time…
Inspired by air industry player in their design (i.e. air vaporizers and storage).
Small amount of LNG  footprints of air vaporizer are acceptable
Unmanned and directly refilled by the truck driver.
Built using modules (assembled on site, faster project schedule…)
LNG inventory being less, safety study are generally “lighter”
In some cases, pressure build up instead of a pump.

## Slide 5
Small Regas Terminal (2)
Common features, most of the time…
Maintenance reduced (motorized parts and instrumentation are very few).
LNG transfer through a flexible hose(emergency disconnection system a dry break coupling).
Boil of gas generated naturally (contained in pressurize tank)
Air vaporizers preferred (simplicity nonoperating expenditures).
These terminals almost never go beyond 0.3 MTPA (so far).
(Some terminals <1 MTPA but uses conventional technologies)

## Slide 6
Safety matters
LNG is new to many industries Bunkering, LPG turning to LNG, Gas station.
LNG  run by Oil & Gas companies with strong safety culture
The small scale industry business development of faster than technical and safety guidelines
 Big challenge to preserve a good image and make the business sustainable (with respect to newcomers not having all a safety culture).